## Slide 1
Capstone Project 3
Intelligent Cylinder Head Bolt Measurement System
Antony Akwalu
Gaurawa Kovida
Nipun Gunarathne
Mate Ganbat
Sass Bendeguz
Szabo Vilmos Benedek
Team Members

## Slide 2
Team Structure & Workflow
Organization: Division into three specialized sub-teams:
              Hardware: Soldering, circuit construction, sensor integration.
      Software: Code structure, DAQ system, UI generation.
      Measurement: Calibration, execution, data analysis
Role | Member
Hardware | Nipun
 | Antony
Software | Mate
 | Kovida
Measurement | Benedek
 | Bendeguz

## Slide 3
Analyze stress and load states of bolts and cylinder heads.
Build and calibrate a functional transducer system.
Compare tightening processes using professional data acquisition.
Demonstrate professional project management through sub-team division.
Project Goals

## Slide 4
System Overview
Core Components: Force transducer, HX711 Signal Amplifier, ESP32 Micro-controller
The force transducer utilizes a hardened steel ring as an elastic element that deforms under the bolt's clamping load, which is detected by dual-grid strain gauges bonded to its surface.
This mechanical deformation is converted into a digital signal through a Full Wheatstone Bridge circuit and a 24-bit HX711 amplifier, allowing the ESP32 microcontroller to precisely quantify the high compressive forces

## Slide 5
Steps of the Build
Soldering and its Basics
Soldering is a fundamental process used to join electrical components by melting a filler metal (tin) into the joint
Basics
Heat both parts sufficiently
Achieve shiny and cone-shaped joints

## Slide 6
Strain gauges
We utilised the BX120-2BB Strain Gauge , a dual-grid sensor designed to measure deformation in two perpendicular directions.
The Elastic Element - a hardened steel ring (Model: IR 15x20x14 IS1-OF-XL). This component serves as the transducer body
The Sensor (BX120-2BB):The gauge features two distinct measuring grids:
Direction 1 (Red Arrow): Aligned to measure the primary axial strain (compression of the ring).
Direction 2 (Blue Arrow): Aligned to measure the transverse strain

## Slide 7
3. The Wheatstone Bridge
A Wheatstone bridge is an electrical circuit used to measure an unknown resistance by balancing two legs of a bridge circuit, one of which includes the unknown component
Prototype Wiring of the Wheatstone

## Slide 8
4. Signal Conditioning (HX711 Integration)
The signal output from the Wheatstone bridge is an analog voltage in the millivolt range, which is too weak and noisy for the microcontroller to read directly.
To solve this, we integrated the HX711 module, a 24-bit Analog-to-Digital Converter (ADC) designed for high-precision weigh scales.
Functions
  Amplification of signal from bridge
  Digitization of the analog voltage into a digital data stream that the ESP32 can process

## Slide 9
5. Microcontroller Interfacing (ESP32)
The ESP32 is a high-performance, low-cost microcontroller designed for complex data processing and multi-sensor management. In this project, it acts as the "brain" of the DAQ system, using its high clock speed to capture and stream synchronized data from nine measurement channels simultaneously

## Slide 10
Final assembly
The final assembly integrates the mechanical, electrical, and software components into a unified 9-channel measurement station.
Physical & Electrical Integration
Sensor Array: Eight custom transducers are fitted to the cylinder head bolts, while a ninth channel is dedicated to an instrumented torque wrench.
Signal Chain: Each transducer's Full Wheatstone Bridge connects to an HX711 ADC module, which amplifies and digitizes the raw force data.
Control Hub: All nine HX711 modules are wired to an ESP32 microcontroller.

## Slide 11
Channels 1-8 (Bolts): Connected directly to the cylinder head bolts to capture the clamping force distribution across the engine block.
Channel 9 (Wrench): Connected to the instrumented torque wrench. This channel allows us to correlate the applied torque (input) with the resulting clamping force (output) on the bolts.

## Slide 12
DAQ software architecture (NodeMCU ESP32)
Direct Parallel Interface: 18 GPIO pins used  9 clock + 9 data  Maximum signal speed
Sampling rate: 10Hz (100ms interval) using non blocking timers.
Calibration: Hard coded sensitivity slopes for all the 9 channels to ensure efficient processing.
Output: Live CSV stream to PC via Serial (9600 baud) for excel integration.

## Slide 13
Operation
1.Input
Code iterates through the array.
Uses 18 dedicated GPIO pins to read raw signals from all 9 sensors simultaneously.
Non-blocking loop executes exactly every 100ms.
2.Processing
Subtracts the stored from the raw reading.
Divides by the hard coded slope to convert to Newtons or Nm.
3.Output
Makes a single CSV string that includes all the 9 values + timestamp.
Streams via USB serial directly to Excel data streamer for live visualization,

## Slide 14
Calibration
Procedure:
Each bolt was individually stressed with known reference loads.
Linear regression was used to calculate the specific sensitivity (Slope) for each sensor.
Implementation:
To save processor cycles during the measurement loop, these values were hard coded into the firmware arrays.
Verification:
System was tared with a 100g weight.
Removing the weight resulted in -100 reading confirming perfect linearity and slope accuracy.

## Slide 15
Experimental Measurement Protocol
Bolt tightening
Bolt loosening

## Slide 16
Tested Sequences
Sequence A
Sequence B

## Slide 17
Application of Torque – Graphical Representation
11
1 min
2 min
3 min
4 min
6 min
5 min

## Slide 18
Sequence B
Sequence A
Clamping force Distribution – Graphical Analysis

## Slide 19
 | Sequence A (Standard) | Sequence B (Reversed)
Order | B-C-F-G-H-E-D-A | H-E-D-A-B-C-F-G
Max Force | ~52,000 units (Bolt E) | ~48,700 units (Bolt E)
Min Force | ~24,200 units (Bolt F) | ~26,300 units (Bolt F)
Variation | High (~27,800) | Lower (~22,350)
Uniformity | Poor Distribution | Marginal Improvement
Analysis Summary

## Slide 20
Why differences?
The observation:
Both sequences used “crisscross” pattern, but sequence B resulted less variation and higher minimum clamping force.
Probable cause:
Uneven deformation of the bolts because of repeated tightening and loosening.
Uneven distribution of lubricant.
Wear and deformation of the threads in the block.(torque to yield bolts)

## Slide 21
Conclusion
Torque Tension:
70Nm of input torque resulted in clamping forces varying by over 27000 units.
Friction and mechanics dominate the results.
System viability:
The custom ESP32 DAQ successfully captured transient phenomena at 10Hz,
It shows that even the low-cost hardware can deliver professional engineering insights.
External factors:
Usage of lubricant resulted in improved clamping forces.
Even with perfect tightening sequence, factors like uniform lubrication plays a key role.

## Slide 22
Thank you!